## Slide 1: Arduino Part 1
Topics:
Microcontrollers
Programming Basics: structure and variables
Digital Output
Analog to Digital Conversion

## Slide 2: What is a Microcontroller
A small computer on a single chip
  containing a processor, memory, and input/output
Typically "embedded" inside some device that they control
A microcontroller is often small and low cost
Examples
www.mikroe.com/chapters/view/1

## Slide 3: What is a Development Board
A printed circuit board designed to facilitate work with a particular microcontroller.
Typical components include:
  power circuit
  programming interface
  basic input; usually buttons and LEDs
  I/O pins

## Slide 4: The Arduino Development Board
Making-robots-with-arduino.pdf

## Slide 5: The Arduino Microcontroller: Atmel ARV Atmega 328
Making-robots-with-arduino.pdf
Specification

## Slide 6: What is the Arduino
todbot.com/blog/bionicarduino

## Slide 7: Getting Started
Check out: http://arduino.cc/en/Guide/HomePage
  Download & install the Arduino environment (IDE)
  Connect the board to your computer via the UBS cable
  If needed, install the drivers (not needed in lab)
  Launch the Arduino IDE
  Select your board
  Select your serial port
  Open the blink example
  Upload the program

## Slide 8: Try It: Connect the USB Cable
todbot.com/blog/bionicarduino

## Slide 9: Arduino IDE
See: http://arduino.cc/en/Guide/Environment for more information

## Slide 10: Select Serial Port and Board

## Slide 11: Status Messages
todbot.com/blog/bionicarduino

## Slide 12
todbot.com/blog/bionicarduino

## Slide 13: Add an External LED to pin 13
File > Examples > Digital > Blink
LED’s have polarity
  Negative indicated by flat side of the housing and a short leg
www.instructables.com

## Slide 14: Terminology

## Slide 15: Add an External LED to pin 13

## Slide 16: A Little Bit About Programming
Code is case sensitive
Statements are commands and must end with a semi-colon
Comments follow a // or begin with /* and end with */
loop and setup

## Slide 17: Our First Program

## Slide 18: Digital I/0
pinMode(pin, mode)
  Sets pin to either INPUT or OUTPUT
digitalRead(pin)
  Reads HIGH or LOW from a pin
digitalWrite(pin, value)
  Writes HIGH or LOW to a pin
Electronic stuff
  Output pins can provide 40 mA of current
  Writing HIGH to an input pin installs a 20KΩ pullup
www.mikroe.com/chapters/view/1

## Slide 19: Arduino Timing
delay(ms)
  Pauses for a few milliseconds
delayMicroseconds(us)
  Pauses for a few microseconds
More commands: arduino.cc/en/Reference/HomePage

## Slide 20: Digital? Analog?
Digital has two values: on and off
Analog has many (infinite) values
Computers don’t really do analog, they quantize
Remember the 6 analog input pins---here’s how they work
todbot.com/blog/bionicarduino

## Slide 21: Bits and Bytes

## Slide 22: Variables
www3.ntu.edu.sg

## Slide 23: Putting It Together
Complete the sketch (program) below.
What output will be generated by this program?
What if the schematic were changed? 
www.ladyada.net/learn/arduino

## Slide 24: Some References
www.arduino.cc
www.ladyada.net/learn/arduino
www.EarthshineElectronics.com